## Slide 1
May 14, 2025 - Meeting
Accessibility Advisory Board
Tactile Wayfinding—Improving Access for People with Vision Disabilities

## Slide 2: Who are we talking about?
The large majority have some vision
The large majority become vision disabled after the age of 60
The large majority have some degree of age-related hearing loss
Diabetic Retinopathy
Photo credits: ADB Staff
Retinitis pigmentosa
Macular degeneration

## Slide 3: People with low vision may have:
Loss of visual acuity (sharpness of vision)
Loss of visual field
Difficulty seeing at night
Sensitive to glare
Reduced contrast sensitivity
Photo credit: ADB Staff

## Slide 4: Tools for travel
Many People with Visual Disabilities (PVDs) use no obvious tool!
Long white cane—scans the environment approximately where the next foot will fall
Dog guide—handler gives directions; dog provides safety; only 5-10% of PVD
Low vision aids—monocular; primarily for spot checking, especially signs
Apps—helpful to some PVD; never a substitute for providing accessible information

## Slide 5: Techniques for travel
Listening—most important technique
Vehicle sounds to determine onset of walk interval at signalized crossing— surge of through traffic in near lane
Vehicle sounds to determine direction (align to cross)—primarily traffic parallel to crosswalk
Vehicle sounds to detect traffic gaps and yielding vehicles
Many PVDs have never been taught techniques for maximizing use of their low vision, or taught to use any special techniques
Photo credit: Janet Barlow-SOMA 2016 presentation

## Slide 6: Wayfinding Challenges

## Slide 7: Finding non-corner crossings:
Photo credit: www.pedbikeimages.org / Toole Design Group
Mid-block crossings
Roundabouts

## Slide 8: Recognizing the boundary of a street with curb ramp without detectable warning surface
Photo Credit: Sean Bennett, Fig. 1. Representative intersection of sidewalk and road, including a diagonal curb ramp Download Scientific Figure on ResearchGate (researchgate.net)

## Slide 9: Avoiding separated bike lanes at sidewalk level
Photo credit: Toole Design

## Slide 10: Finding Transit Facilities
Guidance to:
  Fare-gates, ticket machines
  Platforms
  Elevators/escalators
  Bus transfer areas
  Locating bus stops,
  Floating transit islands

## Slide 11: Wayfinding Options

## Slide 12
The Transportation Research Board published the final document that discusses the requirements for successful tactile wayfinding:
New research discusses how different tactile walking surface indicators (TWSIs) can be used in complex transportation and crossing settings.
Where other design cues may be inconsistent, confusing, misleading, or missing to provide wayfinding information to people who are blind or visually impaired.
The results of experiments on detectability, discriminability, and application of TWSIs along with
Guidelines for planning, designing, constructing, and maintaining TWSIs in different transportation and crossing settings.

## Slide 13: Tactile Walking Surface Indicator (TWSI)
Generic term for 3 types of walking surfaces to aid wayfinding for pedestrians with vision disabilities:
Detectable warning surface (DWS)
  aka: truncated domes, or domes
Tactile direction indicator (TDI)
  aka: raised bars, guiding bars, or directional bars
Tactile warning delineator (TWD)
  aka: trapezoidal delineator, or trapezoid
Photo Credit: Beezy Bentzen
Photo Credit: Linda Myers
Photo Credit: John Robert McPherson, CC0,via Wikimedia Commons

## Slide 14: Detectable Warning Surface
What should pedestrians who are vision disabled think when they encounter truncated dome DWS?
I should stop and figure out whether I’m at a street or transit platform and prepare to either cross the street or board the vehicle.
If I’m at a street, I should explore for cues to help me align in the direction of the crosswalk.
The domes should NOT be used as a cue for aligning to cross.
Photo Credit: Pi.1415926535, CC BY-SA 3.0
https://commons.wikimedia.org/w/index.php?curid=91289870

## Slide 15: Tactile Direction Indicator (TDI) – Bars
What should pedestrians who are vision disabled think when they encounter TDI bars?
It depends on environmental context and width of the surface!
If 12 in. (4 bars): follow the bars parallel
If 24 in. follow the bars perpendicular
Photo Credit: ADB Staff
If the bars are running in parallel and extending some distance, then this is a surface I can follow.
I can follow it on either side if there is room.
I should not encounter obstacles if I am following along while walking beside it.

## Slide 16: Tactile Direction Indicators – Alignment Bars
2 ft. x 2 ft. square of bars
Orient bars perpendicular to the direction of travel across crosswalk
Photo Credit: ADB Staff
Photo Credit: Steve Graham
If a “patch” of raised bars is located near a street crossing, and near the end of or just behind a DWS, I can use it to establish an accurate alignment with the crosswalk.

## Slide 17: Tactile Warning Delineator (TWD)
What should pedestrians who are vision disabled think when they encounter a trapezoidal TWD?
I should not cross this surface because there is danger of a crash with a bicycle or other hazard on the other side.
Photo credits: Linda Myers

## Slide 18: Specifications for TWSIs
TCRP Research Report 248, Figure 5
TCRP Research Report 248, Figure 9
Tactile Direction Indicator (TDI)
Detectable Warning Surface (DWS)
Tactile Warning Delineator (TWD)
TCRP Research Report 248, Figure 7

## Slide 19: Bus Stops, Bus Boarding Islands, and Transit Centers
TCRP Research Report 248, Figure 23
TCRP Research Report 248, Figure 24
TCRP Research Report 248, Figure 25
Detectable Warning Surface (DWS)
Tactile Direction Indicator (TDI)
Tactile Warning Delineator (TWD)

## Slide 20: Crossing Applications
TWSIs can help people who are blind or have low vision identify the following items:
  Location where a street intersects the pedestrian path
  Boundary between pedestrian path and the path of motor vehicles, bicyclists, or trains
  Alignment of the street crossing
  Changes in alignment for the pedestrian path
  Transitions between shared-use paths and separated bicyclist and pedestrian paths
Use good design geometry should do most of the work;
TWSIs should be a supplement, not a primary measure

## Slide 21: Crossing Median - Separated Bicycle Facility

## Slide 22: Separated Bike- Ped Facilities
TCRP Research Report 248, Figure 39

## Slide 23: Bicycle Ramp Applications
Used to transition between on-street bicycle lane and shared-use path
TCRP Research Report 248, Figure 40

## Slide 24: Implementation Challenges

## Slide 25: Implementation
Selecting TWSI materials
  Maximizing durability and detectability
  Minimize future maintenance
Guidance for Orientation and Mobility (O&M) Professionals
  Training potential users
  Discussion of basic principles using terminology familiar to O&M professionals
    “Domes”, “Raised Bars”, and “Trapezoid”
  Discussion of locations where different kinds of TWSIs might be found
  Cane technique for detecting TWSIs
  Strategies for using TWSIs

## Slide 26: Implementation Activities
Assessing effectiveness of tactile wayfinding system after installation
Maintenance
  System design to minimize future maintenance
  Routine maintenance activities
  Maintaining wayfinding during utility and construction work
Developing Standards
  Designating a team
  Affording the team?

## Slide 27
Tactile Warning Delineator (TWD)

## Slide 28: Case studies
Brief case studies on four U.S. agencies
  Bay Area Rapid Transit (BART), San Francisco Bay Area, California
  Los Angeles Metro Rail, Los Angeles County, California
  City of San Francisco, California
  City of Seattle, Washington

## Slide 29
Tactile Warning Delineator (TWD)

## Slide 30
Questions
and
Comments
Tactile Wayfinding

## Slide 31: Parallel Curb Ramps 6’ wide

## Slide 32
PROWAG PR (2013) R304.3.1 Turning Space
A turning space 1.2 m (4.0 ft) minimum by 1.2 m (4.0 ft) minimum shall be provided at the bottom of the curb ramp and shall be permitted to overlap other turning spaces and clear spaces.
If the turning space is constrained on 2 or more sides, the turning space shall be 1.2 m (4.0 ft) minimum by 1.5 m (5.0 ft). The 1.5 m (5.0 ft) dimension shall be provided in the direction of the pedestrian street crossing.
PROWAG FR (2023) R304.3.4 Landings
Landings shall be provided at the bottom of parallel curb ramps. Landings shall be 48 inches (4.0 ft) wide minimum by 48 inches (4.0 ft) long minimum. The slope of the landing, measured parallel to the direction of travel on the curb ramp run, shall be permitted to be equal to or less than the slope of the roadway or the cross slope of the crosswalk as specified by R302.5..
Access Board- Public Right of way accessibility guidelines (PROWAG)

## Slide 33: Parallel curb ramps – California Building Code (CBC)
11B-406.3.2 Turning space. A turning space 48 inches minimum by 48 inches minimum shall be provided at the bottom of the curb ramp. The slope of the turning space in all directions shall be 1:48 maximum.

## Slide 34: 2019 Intermediate Code Changes
DSA STATEMENT OF REASONS:
This change reformats Section 11B-705.1.2.2 to present detectable warnings requirements separately for perpendicular and parallel curb ramps. Revised detectable warning requirements are also provided for parallel curb ramps with one entrance/exit point (i.e. transition from the turning space to the gutter, street or highway) and those with two entrance/exit points – as may be found in parking lots where a median has accessible parking on both sides of an island.
The amendment language requires the turning space to include a 36” minimum width passage without detectable warnings so pedestrians may travel through the turning space without passing over the detectable warnings. This provision responds to numerous comments from wheelchair users who experience pain when travelling over extended lengths of detectable warnings.

## Slide 35: Parallel Curb ramps - CBC
Exceptions:
1. Where it is technically infeasible to provide a minimum 72 inches wide turning space, as measured perpendicular to the curb, the depth of detectable warnings may be reduced to 24 inches minimum.
2.Existing parallel curb ramps with detectable warnings in compliance with the code requirements in effect at the time of installation shall not be required to provide a minimum 36 inches wide portion of the turning space without detectable warnings.
11B-705.1.2.2.2.1 One entrance/exit point. Where the turning space has one entrance/exit point other than the sloped ramp segments, detectable warnings shall be 36 inches deep, as measured perpendicular to the curb, and the turning space shall provide minimum 36 inches wide portion without detectable warnings to allow pedestrian travel in the direction of the sidewalk without travelling over the detectable warnings.

## Slide 36: Parallel Curb ramps - CBC
Exceptions:
  1. Where it is technically infeasible to provide a minimum 72 inches wide turning space, as measured perpendicular to the curb, the depth of detectable warnings may be reduced to 24 inches minimum.
  2.Existing parallel curb ramps with detectable warnings in compliance with the code requirements in effect at the time of installation shall not be required to provide a minimum 36 inches wide portion of the turning space without detectable warnings.
11B-705.1.2.2.2.2 Two entrance/exit points. Where the turning space has two entrance/exit points other than the sloped ramp segments, detectable warnings shall be 36 inches deep at both entrance/exit points, as measured perpendicular to the curb, and the turning space shall provide a minimum 36 inches wide portion without detectable warnings to allow pedestrian travel in the direction of the sidewalk without travelling over the detectable warnings.

## Slide 37
For existing 4’ wide sidewalks:
Will the wheelchair user will zig-zag to avoid rolling over 4’ long truncated domes?
The green highlighted area indicates the additional square footage needed for the extra 2’.

## Slide 38
Questions
and
Comments
6’ wide parallel curb ramp